## Slide 1: DXing from a City Lot
Gary L. Drasch
K9DJT

## Slide 2: What is DXing and Why???
Wikipedia: Amateur radio operators who specialize in making two way radio contact with other amateurs in distant countries are referred to as "DXers".
It’s a challenge! Not only is propagation required, there is a technique or skill involved. In addition an operator needs the ability to assemble a station which is capable of performing.

## Slide 3: My DXing History
Countries Worked since December 1, 2010

## Slide 4: How do I reach the next plateau?
At this stage of the game I had already:
  upgraded to a dual receiver radio (FT-2000)
  bought and refurbished an amplifier (Desperado)
  Had a 40 foot tower with a tri-band beam.
  Had a trap dipole for 40, 80 and 160 meters.
The answer was the antenna system, but what more could I do on a city lot 120 feet wide and 90 feet deep?
---And the wife doesn’t want to move to the country!!!

## Slide 5: But my Antenna System is working…
They don’t need to be resonant…
They don’t need to be certain height…
They don’t necessarily need to be any particular shape…
I was reminded of something I already knew while attending the W9DXCC convention in Chicago this year, and that was…
All antennas work!
All you need is a good antenna tuner which will create a conjugate match, and they’ll work!

## Slide 6: Efficiency is the difference!
How efficiently is the system actually working?
How much loss is created by SWR?
How much loss is caused by the tuner itself?
Will a resonant antenna work better?
Should it be a vertical or dipole in nature?
It is not just the antenna, transmission line or tuner…
It is the antenna SYSTEM as a whole!
Just ask the Curmudge!

## Slide 7: System Evaluation by Band:
10, 15 and 20 meters: KT-34A 4-ele beam, excellent performance, old RG-8U solid dielectric coax. Element-to-boom connectors need replacement.
12/17 meters: No specific antenna. Have been matching tri-bander with mediocre results.
30 meters: No antenna
40, 80 and 160 meters: Trap dipole which works as expected. Narrow bandwidth and more of a cloud warmer than a DX antenna.

## Slide 8: Project Decision by Band
10, 15 and 20 meters: Lower KT-34A and replace element-to-boom connectors. Replace RG-8U coax with 7/8” hardline.
12/17 meters: Construct my own elements based on the Cushcraft A3WS, and attach to bottom of KT-34A boom. Share the 7/8” hardline with KT-34A and the below.
30/40 meters: Construct half-Slopers using the tower and burying a radial system into the lawn. Share 7/8” hardline with beam.
The 7/8” hardline will be switched via a mechanical rotary switch utilizing “N” connectors

## Slide 9: Project Decision by Band (Continued)
80 meters: Construct an Inverted-L utilizing the in-ground radial system and an additional shared 7/8” hardline.
160 meters: Construct a Gamma Matched inverted-L utilizing the tower and the in-ground radial system. It will share the 7/8” hardline mentioned above.
Antennas will be matched and switched to the 7/8” at the base of the tower.

## Slide 10: My Starting Point
KLM KT-34A
Ugly Balun –
Feeding 40, 80 & 160
trap dipole
Tapered Tower Top

## Slide 11: Off the Air…
Customized straight section
Element-Boom Connectors
7/8” Hardline
Flat Top-plate
Removal of tri-bander and tower modifications
Preventative Maintenance

## Slide 12: Rotor and Switch Installation…
6x6x6 Electrical
Enclosure
Modified Rotor Plate
Half-Sloper interface and bead-choke
½” Hardline

## Slide 13: The Making of 12/17 Meter Elements
Fiberglass
17M element
Homebrew 12M
Coaxial Trap

## Slide 14: 12/17 Elements, Truss and Thrust Bearing
Thrust Bearing
Bead Chokes

## Slide 15: Ready to go back up!!!

## Slide 16: Raising it back up!!!

## Slide 17: Fastening the Thrust Bearing

## Slide 18: Adding the Low-Bands

## Slide 19: What it Actually Looks Like!
30M Half-Sloper
40M Half-Sloper
160M Leg
160M Gamma
Match
80M Inverted-L
Insulating Tower from Aluminum Siding

## Slide 20: Radial System Layout

## Slide 21: Matching the 80M Inverted-L

## Slide 22: Matching the 160M Gamma
Gamma and Length still need tweaking!

## Slide 23: SWR without a tuner…
Chart: 
| f1 | f2 | f3 | f4 | f5
10M | 3 | 2 | 2 | 3 | 3.5
12M | 1 | 1 | 1 | 1 | 1
15M | 1.6 | 1.2 | 1.1 | 1.1 | 1.2
17M | 1.1 | 1.1 | 1.1 | 1.1 | 1.1
20M | 1.3 | 1.3 | 1.25 | 1.2 | 1.15

## Slide 24: SWR without a tuner…
Chart: 
| f1 | f2 | f3 | f4 | f5
30M | 1.2 | 1.2 | 1.2 | 1.2 | 1.2
40M | 1.4 | 1.4 | 1.3 | 1.2 | 1.15
80M | 1.75 | 1.15 | 1 | 1.2 | 2
160M | 1.4 | 1.2 | 1.1 | 1.15 | 1.5

## Slide 25: End Result
Total Transmission line loss (Including loss due to SWR)
= .014 db @160M to .249 db @10M
Antenna Tuner no longer required
Instant Band Switching (Almost…)
If I can hear em, I can work em!!!

## Slide 26: Thank you…
Dit Dit
You are welcome to ask questions on the ORC Forum,
or eMail me at k9djt@sbcglobal.net